## Slide 1
Intel DevCloud Training Module
FPGA Timing Optimization
Misc FSM(D) Timing Tips
Greg Stitt
Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: FSM(D) Timing Optimizations
Only do an assignment on a transition if necessary
case (state_r)
START : begin
if ({a,b,c,d} == 4'b1) begin
count_r <= COUNT_BITS'(1);
done_r <= 1'b0;
state_r <= COMPUTE;
end
end
…..
count_r
a
state_r[0]
AND
b
c
d
case (state_r)
START : begin
count_r <= COUNT_BITS'(1);
if ({a,b,c,d} == 4'b1) begin
done_r <= 1'b0;
state_r <= COMPUTE;
end
end
…..
count_r
state_r[0]
If FPGA doesn’t have a 5-input LUT, requires a hierarchy of smaller LUTS => extra delay
*Assumes one-hot state encoding and that state_r[0] corresponds to START
en
en

## Slide 3: FSM(D) Timing Optimizations
Don’t assign a register in a state if the assignment isn’t needed
  Each state where register is assigned becomes part of enable and/or mux logic
  Usually happens from repeated clearing of register in multiple states
case (state_r)
STATE0 : begin
count_r <= COUNT_BITS'(0);
...
state_r <= STATE1;
end
STATE1 : begin
count_r <= COUNT_BITS'(1);
...
state_r <= COMPUTE;
end
STATE2 : begin
count_r <= count_r + 1’b1;
...
end
count_r
1
OR
en
state_r[1]
state_r[2]
state_r[0]
0
+
1

## Slide 4: FSM(D) Timing Optimizations
Apply general timing optimization techniques
  Don’t chain multiple dependent operations together in a state
  Register outputs when control allows for it
  Don’t reset everything, only state and validity information
  Use register duplication for high fanout
  Convert logic inputs to constants wherever possible
    e.g., comparing a count with a variable instead of a constant