## Slide 1: Addressing Dark Silicon Challenges With Disciplined Approximate Computing
Authored By: Hadi Esmaeilzadeh, Adrian Sampson, Michael Ringenburg, Luis Ceze, Dan Grossman, Doug Burger
Presented by: Tomasz Wiercioch
Notes: Paper published in 2012

## Slide 2: Background/Review
Dark Silicon
  Power restriction
  Not all transistors on a chip can be used at the same time

## Slide 3: the problem
Dark Silicon performance gap
  Optimistic upper bound projections still short of historic improvements
New, much more efficient techniques need to be explored

## Slide 4: The approach
Co-design of Hardware and Software
3 levels of approach
  Programming
    Safe expressions and strong semantics
  Architecture
    Application specific, and energy saving
  Circuit (aka Accelerators)
    For general purpose use

## Slide 5: Disciplined Approximate Programming
Viable approx. languages must be easy and safe
E.g. EnerJ
  Programmer provides annotations
  EnerJ automatically maps approx. vars to low-power applications
  Allows for isolation of approximations
  Static analysis removes need for dynamic checks (“disciplined”)

## Slide 6: Disciplined Approximate Programming
In general:
  Approximation-aware model helps write generalizable approximate programs
  Abstract semantics allow for flexible application of approximation

## Slide 7: Architecture Design for Approximation (Truffle)
Microarchitecture supporting authors’ previous ISA extension
Dual voltage functional units and SRAM
Compatible with other approximation devices
  Custom functional units
  Analog operation/storage
Notes: ISA = Instruction Set Architecture?
Lower voltage = less precise

## Slide 8: Truffle PROs/Cons
Can run approximate and precise instructions (dynamic precision)
  Requires static guarantees from compiler
  Static encoding of precision level for all operations and storage
Co-design simplifies microarchitecture and alleviates fine-grained overhead
Efficiency is limited by processor frontend
Stay tuned for more!

## Slide 9: Approximate Accelerators
Idea: configurable approximate accelerators
  Adapted to replace “hot code” at runtime
  Examples:
    BERET
    Conservation Cores
    DySER
    QsCores

## Slide 10: Novel Data driven idea
Aka Neural Nets
  Trained to be used as application specific accelerators
  May be run on NPUs
    Typically needs deep integration with processor pipeline
  Other hardware (GPUs, FPGAs, FPAAs)
    Can still accelerate operations significantly

## Slide 11: Important Neural Net Questions
What should the programming model look like?
How can a neural network be automatically configured and trained with limited intervention from the programmer?
How should the compilation workflow transform programs to invoke NPUs?
What ISA extensions are necessary to support NPUs?
How can a high-performance, low-power, configurable neural network implementation tightly integrate with the pipeline?

## Slide 12: Conclusions
Is approximate computing viable?
  Yes!
  May help combat dark silicon performance gap
Language and runtime techniques are critical
  Express and enforce reliability constraints
  Necessary for application of new technologies at each level

## Slide 13: Sample Questions
Truffle refers to a
  Microfungus
  Microarchitecture
  Macroarchitecture
  Approximate Accelerator
Answer: B

## Slide 14: Sample Questions
What are the 3 targets of developing approximate computing?
(select all that apply)
  User
  Programming
  Architecture
  Circuit (Accelerator)
Answer: B, C, D

## Slide 15: Sample Questions
The Dark Silicon performance gap is
  The inability of darker silicon to preform as well as translucent silicone
  The difference between Moore’s law and current production capabilities
  A made-up metric to get funding for approximate computing projects
  The deviation of projected conventional advancements in microprocessors when compared against historical performance scaling
Answer: D