## Slide 1: Dense Approximate Storage in Phase Changing Memory
Jacob Nelson, Adrian Sampson, and Luis Ceze University of Washington

## Slide 2: What is Phase Changing Memory?
A type of Non-volatile Random-Access Memory
Stores Digital Data by quantizing and Analog Signal by varying the varying electrical of a material
  Material is largely Chalcogenide glass
A PCM cell can store more data in a single cell by using a non-binary scale
  This creates the higher density storage medium
The limit on density on is the noise caused by the resistance properties of the material

## Slide 3: Multi-Level Cell Phase Changing Memory
Fun Fact: This is the technology that is used for storing data on Blu-ray Disks

## Slide 4: Approximate Storage in PCM Cells
Supports more resistance values than are reliably writable or readable
Write errors- Cells set to the resistance value of the material incorrectly
Read Errors- Cell is not able to accurately measure the material’s resistance value within timing constraint for a read operation

## Slide 5: Writing to an Approximate MLC
Data is stored by controlling the crystallization of the chalcogenide glass through a shaped write pulse to the cells heating element
The same pulse can lead to different resistances when applied to different cells in the array or to the same cell at different times

## Slide 6: Solutions
Verification Step
  Use a read back to check that the stored value is same as the written value
  Continue to write until you get the same value
  Gives Precise Vales
Leads to High Write Latency, energy usage and heater wear
Can Implement limited precision by using an error bound.
Uses a verification step until the returned value is within the error bound

## Slide 7: Reading from an Approximate MLC
Read from an ADC to sense resistance
Integrating ADC uses a capacitor to measure the amount of time required to discharge through the cell
  Read time scales exponentially with the number of bits
Successive approximation ADC uses a sample and hold circuit to refine measurement over multiple cycles
  Scales Linearly
An approximate array can trade precision for latency

## Slide 8: Evaluation
Modeled three types of errors
  Write Error- added a random integer taken from a normal distribution to the value stored in each cell
  Read Error- truncated bits read from each cell
  Heat Wear- replaced the value in randomly chosen subset of cells with a random value

## Slide 9: Evaluation Continued
8 bits per PCM allowing a write error of 3, truncating one bit on read and 1 heat wear error out of a 1000
When compressed JPEG had 48,409 significant pixel differences
Approximate Images shows 45,637