## Slide 1: Security in Approximate Computing and Approximate Computing for Security: Challenges and Opportunities
By Weiqiang Liu , Chongyan Gu , Máire O’Neill, Gang Qu , Paolo Montuschi , And Fabrizio Lombardi

## Slide 2: Technology Background
Approximate computing introduces security vulnerabilities
  Existing work on the security of approximate computing covers threat models, countermeasures, and evaluations
Security threats of approximate computing from the perspective of…….
  Hardware, namely, side-channel analysis (SCA), reverse engineering, cloning/counterfeiting, and active attacks
  Cryptography, namely Homomorphic Encryption, Post-Quantum Algorithims, and Learning with Errors problems

## Slide 3: Intro to Hardware Security and Cryptography
Hardware Trojans
  Any modification or addition to a circuit for malicious purpose
Logic Locking
Physical Unclonable Function
Side-Channel Analysis

## Slide 4: Intro to Hardware Security and Cryptography
Hardware Trojans
Logic Locking
  Hiding important information, for example, functionality and implementation, related to a circuit by inserting additional logic into the original design.
Physical Unclonable Function
Side-Channel Analysis

## Slide 5: Intro to Hardware Security and Cryptography
Hardware Trojans
Logic Locking
Physical Unclonable Function
  Utilizes the inherent process variations during manufacturing to generate a unique digital fingerprint that is intrinsic to the device itself.
Side-Channel Analysis

## Slide 6: Intro to Hardware Security and Cryptography
Hardware Trojans
Logic Locking
Physical Unclonable Function
Side-Channel Analysis
  Can reveal sensitive information from the implementation of security/cryptographic schemes by observing their electrical characteristics while operating

## Slide 7: Intro to Hardware Security and Cryptography
Homomorphic Encryption
  Cryptographic approach that can perform calculations directly on encrypted data without needing to decrypt the data first.
Post Quantum Cryptography (PQC)
  Quantum computers may break today’s most popular public-key cryptographic systems, including RSA, elliptic-curve cryptography, DSA, and ECDSA.
Lattice Based Cryptography
  Most popular branches of PQC due to its versatility, its security hardness, and the fact that it can be constructed efficiently on various computing platforms.

## Slide 8: Security Threats in Approx. Computing
Organized by confirmed vs. potential security threats
General -- Affects many applications
Attacks
Deanonymization, the only referenced DRAM term outside previous lectures
Voltage Scaling
DRAM
SRAM
Adders
PCM
Applications
Image Processing
Pattern Recognition
Data Analysis

## Slide 9: Security Threats in Approx. Computing: Approximate Arithmetic Circuits
Malicious modification of registers
  Force higher energy consumption through input manipulation
Hardware Trojans
Voltage scaling
Reverse Engineering
+
ECC
Inputs
Adder
Output
0
1
1
0
0
1
1
0
2
Simplified truncation logic

## Slide 10: Security Threats in Approx. Computing: Approximate Arithmetic Circuits
Malicious modification of registers
  Force higher energy consumption through input manipulation
Hardware Trojans
Voltage scaling
Reverse Engineering
+
ECC
Inputs
Adder
Output
Effect: Increase power consumption through overworking ECC
0
1
1
0
0
1
1
0
2
Simplified truncation logic

## Slide 11: Security Threats in Approx. Computing: Approximate Arithmetic Circuits
Malicious modification of registers
  Force higher energy consumption through input manipulation
Hardware Trojans
Voltage scaling
Reverse Engineering
+
ECC
Inputs
Adder
Output
Effect: Increase power consumption through overworking ECC
Effect: Decrease output quality without user specification, fools user
0
1
1
0
0
1
1
0
6
Simplified truncation logic

## Slide 12: Security Threats in Approx. Computing: Approximate Arithmetic Circuits
Malicious modification of registers
Hardware Trojans:
  Preying on control signals usually required by approximate logic
  Preying on additional ECC module
  Preying on more predictable transition probabilities
Voltage scaling
Reverse Engineering
Sample Hardware Trojan
Resistor
Transistor

## Slide 13: Security Threats in Approx. Computing: Approximate Arithmetic Circuits
Malicious modification of registers
Hardware Trojans
Voltage scaling: Create circuit anomalies by changing VDD
  Increased propagation delay, change chip characteristics -> invalid PUF-like keys (physically-unclonable functions)
  (Over-scaling to produce signal cross-talk)
Reverse Engineering
Sample process for creating a PUF – Uniquely identifies an arbitrary IC sample

## Slide 14: Security Threats in Approx. Computing: Approximate Arithmetic Circuits
Malicious modification of registers
Hardware Trojans
Voltage scaling
Reverse Engineering: Attackers reconstructing a circuit design from a physical copy
  Increased obfuscation from additional control logic
  RE’d circuit will be approximate, not precise logic
Sample process for creating a PUF – Uniquely identifies an arbitrary IC sample

## Slide 15: Security Threats in Approx. Computing: Approximate Storage
DRAM approximation:
  Refresh rate can only fall so much before errors are unrecoverable
  Attackers can force this threshold to be met via register manipulation of A) DRAM refresh counter or B) configuration signal
SRAM Approximation
PCM Approximation
10
User-configured refresh rate
DRAM block
0
Refresh signal

## Slide 16: Security Threats in Approx. Computing: Approximate Storage
DRAM approximation
SRAM Approximation
  Register manipulation applies voltage scaling to MSBs and LSBs instead of just LSBs
PCM Approximation

## Slide 17: Security Threats in Approx. Computing: Approximate Storage
DRAM approximation
SRAM Approximation
PCM Approximation
  Many manipulatable signals to A) Obliterate approximate information or B) Approximate what should have been precise
0.1
1V
x
Vdd
0
0
Voltage scaling constant
Variable scaling ratio
Select = Should approximate?

## Slide 18: Approx. Computing for Security
Applies in two(?) main topic areas + machine learning

## Slide 19: Approx. Computing for Security: Cryptography
Postquantum cryptography:
  Approximate random sampler
  Approximate multiplier
  Allows 35% less circuit area, 23% power reduction, minimal decrease in output entropy
Homomorphic Encryption:
  Makes significant use of modular arithmetic
  Approx . Hardware to simulate ring learning with errors (RLWE) for linear instead of exponential time complexity (!!!)
ApproxHash:
  Replace adders with approx. adders for approx. SHA-1
  Less relevant to modern security since SHA-1 is deprecated
Bitcoin Mining:
  Operational costs ∝ energy consumption
  Approx. arithmetic using less energy = more efficient mining

## Slide 20: Approx. Computing for Security: Hardware Security
Information Hiding for Approximate Computing
  Steganography using approximate operators
VOS-Based Authentication

## Slide 21: Approx. Computing for Security: Hardware Security
Information Hiding for Approximate Computing
VOS-Based Authentication
  Unmasks process variation for soft device authentication
  Can be used for lightweight IoT fingerprinting

## Slide 22: Approx. Computing for ML-Based Security [Violations]
Side-Channel Analysis (SCA) of Cryptographic Algorithms
  SVM and Random-Forest networks to analyze side channel data
PUF
  ML-based methods for determining PUF signatures can be greatly accelerated through approx. computing
Logic Obfuscation

## Slide 23: Approx. Computing for ML-Based Security [Violations]
Side-Channel Analysis (SCA) of Cryptographic Algorithms
PUF
Logic Obfuscation/Locking: Focus on Boolean Satisfiability (SAT) attack
  Typical approaches involve finding all wrong keys through trial and error – last remaining key must be correct
  Proposes finding general groups of wrong keys for much smaller time complexity
Concept of logic locking – True functionality is obscured without key

## Slide 24: Future Research
Error Manipulation
Characterizing the errors generated by approximate designs could be helpful in identifying malicious errors inserted by an adversary.
    For example, a threshold value could be used for errors of approximate designs. Any error that goes beyond the threshold will be considered as a potential malicious attack.

## Slide 25: Future Research
Testing
  In addition to the objectives for normal testing, testing techniques for approximate computing need to consider whether the approximate mechanism is deterministic or nondeterministic and whether it is static or dynamic.
Hardware Trojans
Countermeasures to Attacks on Approximate Computing

## Slide 26: Future Research
Testing
Hardware Trojans
  Approximate computing could change the transition probability of certain signals dramatically. Such change could make the trigger signal of an HT easier to be detected, and it could also introduce rare signal values that can be used as the trigger.
Countermeasures to Attacks on Approximate Computing

## Slide 27: Future Research
Testing
Hardware Trojans
Countermeasures to Attacks on Approximate Computing
  Most of the existing works on the vulnerability of and attacks to approximate computing have countermeasures as well
    However, their main contribution is on the discovery of new vulnerabilities and attacks.
    Countermeasures are normally simple and straightforward.

## Slide 28: Future Research
Security in Cross-Layer Approx Comp.
  In the future, it will be necessary to perform cross-layer security analysis for approximate computing.
Security of Approx Mem.
  Emerging nonvolatile memory technologies, such as resistive random access memory (RRAM) and magnetic random access memory (MRAM), have become attractive for future memory hierarchies.

## Slide 29: Future Research
Approximate PUF
  It is worth investigating the feasibility of building approximate processor-based intrinsic PUFs for the specific system- or architecture-level applications.
Hardeware Trojan Detection
  Recently, machine learning-based approaches, such as NNs, have been proposed for HT detection.

## Slide 30: Conclusion
Core challenges in approximate computing is how to balance security, performance, and errors
    Research on security-related challenges and opportunities for approximate computing has been neglected to some extent
    Currently, security in/for approximate computing has not been widely studied. In particular, the utilization of approximate computing to enhance security/cryptographic primitives has a promising future.

## Slide 31: Question 1
What are the two classifications for Physically Unclonable Functions (PUF's)
  Big PUF, Small PUF
  Strong PUF, Weak PUF
  Linear PUF, Evolutionary PUF
  Approximate PUF, Conevtional PUF

## Slide 32: Question 2
What are two reasons approximate circuits are more susceptible to Trojan insertion?
  Approximate logic usually is accompanied by additional control logic, which can be hijacked
  Approximate logic can yield more predictable logic transitions, which makes triggering Trojans easier
  Since fewer researchers are in the approximate computing domain, fewer countermeasures are developed for Trojans in this area
  Approximate logic must be decoupled from most other on-chip logic, so it is easier to target

## Slide 33: Question 3
What module is responsible for increased power consumption during attacks on approximate hardware as specified in “Security in Approximate Computing and Approximate Computing for Security”?
  Approximate control signals
  User-configured startup parameters
  ECC (Error correction code) logic
  Coupling logic between approximate and precise circuitry

## Slide 34: Question 4
What are 2 ways Approximate Computing may be susceptible to securty breaches?
  Error Manipulation
  Voltage Encryption
  Voltage Modification
  Approximate-Memory Analysis