## Slide 1: An Approximate Communication Framework for Network-on-Chips
By: Yuechen Chen & Ahmed Louri
Presented By: Alexis Rodriguez

## Slide 2: Background Information
Source: https://techterms.com/definition/network
Notes: Scalability of the design improves since IP can be replaced easily

## Slide 3: Network-on-Chip?
Bus is replaced with a computer network style transmission involving routers, switches, and network interfaces.
Can improve the scalability of a design
Can improve the power efficiency of a design
A different type of interconnect
“…are becoming standard communication solution for connecting cores, caches and memory controllers on chips.” - Paper
Notes: Scalability of the design improves since IP can be replaced easily

## Slide 4: OSI (Open Systems Interconnect) Model
Application
Presentation
Session
Transport
Network
Data link
Physical

## Slide 5: OSI (Open Systems Interconnect) Model
Application
Presentation
Session
Transport
Network
Data link – Flits of data
  Examples: Ethernet, i2c, physical addressing (e.g. MAC address), error control
Physical
Notes: Packets, frames, flits, etc

## Slide 6: Answers To What We Are Looking For
Type of approximation? Hardware, software, communication, algorithmic [Framework]
Approximation strategy? Truncation and compression
How is it done? Automatically
What is being approximated? Float & int
How to determine what to approximate? Code analysis
How much approximation is acceptable? User set
What applications are being targeted? Data being transmitted over the network
Notes: Packets, frames, flits, etc

## Slide 7: What is Being Solved?
Communication takes more time than the computation itself
Communication consumes more energy than the computation itself
Notes: Packets, frames, flits, etc

## Slide 8: How is it Solved?
Approximate Communication Framework
  Software
    Automatically identify parts of code that can be approximated (ints/floats)
    User provides error tolerance then truncate the data, compress it, send it
  Hardware
    Compression/Decompression, Quality Control Table
Notes: Packets, frames, flits, etc

## Slide 9: Software – Error Tolerance
Int
Float
Ex (int):
  32 bit number
  5% Error Tolerance
  100 dec = 0000 0000 0000 0000 0000 0000 0110 0100 bin
  Keep 29 MSB (n = 29)
  96 dec = 0…1100000 bin
  Error = (1-(96/100))100 =4%
Notes: Packets, frames, flits, etc

## Slide 10: Software – Compression
Frequent Data Pattern Compression
MSB is replaced by the Code
Assume 32-bit flit (payload)
Notes: Assume 32 bits, MS

## Slide 11: Software – Truncation/Compression Example
Notes: Error in paper: I1, truncated data would be 0x00500000 therefore it should be code 100, not 011

## Slide 12: Software – Code Analysis
Automatically find error resilient values in code sections and calculate error tolerances based on user input.
  Break down operations into basic operations (Control Flow Graph [CFG])

## Slide 13: Software – Code Analysis

## Slide 14: Hardware

## Slide 15: Hardware
Notes: QCT receives a Read packet with an address.
If Hit, reply back with approximation info: address, datatype, and err tol
If Miss, reply back with “negative”
QCT receives a Read Request packet with an address, data type, and error tol
If it has approx. data, table extracts it. If table has multiple entries then it fills the table. Then it forwards only the address to shared cache/memory

## Slide 16: Results
Setup
  Ran framework in GEM5 simulator
  AxBench Benchmark Suite
    Used to benchmark approximate computing
  Target: 95% Quality
  Compared against other frameworks:
    AxBA
    Quality Control Framework

## Slide 17: Results
Experiments
  1) Compression Rate vs Error Threshold
  2) # of Approx. Packets vs Allowable Error (5%)
    Auto vs Manual
  3) Compression Rate vs Allowable Error (5%)
  4) Network Latency
  5) Dynamic Power & Overhead

## Slide 18: Results - Experiment 1

## Slide 19: Results - Experiment 2

## Slide 20: Results - Experiment 3

## Slide 21: Results - Experiment 4

## Slide 22: Results - Experiment 5
4.79 um2 is less than 1% of total NoC area but this is per NI
“When the supply voltage is 1.0 Volt, the framework incurs a power overhead of 1.7 mW for each NI, which is only 0.025 percent of the NoC static power consumption. Compared to quality control framework [20] and AxBA [19], the proposed framework reduces static power overhead by 35 and 41 percent, respectively.”
Notes: Each NI

## Slide 23: Questions
Question 1
  As approximated packets go up relative to total packets…
    A) Power should go down
    B) Power should go up
    C) Latency should go down
    D) Latency should go up
Answer: A and C

## Slide 24: Questions
Question 2
  Why did the Approx. Comm. Framework for NoC work so well?
    A) Truncated int and float
    B) Compression
    C) Automatic determination of approximate data
    D) Manual determination of approximate data
    E) Truncated float
Answer: A, B, C

## Slide 25: Questions
Question 3
  What part of the OSI model does the Approx Framework for NoC focus on?
    A) Physical Layer
    B) Data Link Layer
    C) Network Layer
    D) Application Layer
Answer: B