## Slide 1: An Overlay-Based Design Approach for Mainstream Reconfigurable Computing
James Coole
PhD student, University of Florida
Aaron Landy
PhD student, University of Florida
Greg Stitt
Associate Professor of ECE, University of Florida
Catapult Workshop
This work is supported by National Science Foundation grant CNS-1149285 and the I/UCRC Program of the National Science Foundation under Grant No. EEC-0642422.

## Slide 2: Introduction
Goal: enable FPGA usage by designers currently targeting GPUs and multi-cores
Problem: order-of-magnitude worse productivity
Productivity bottlenecks
  Register-transfer-level (RTL) design
    Solved by high-level synthesis (HLS)
  Long compile times (hours to days)
    Prevents mainstream methodologies
__kernel void convolve(float *s) {…}
OpenCL
HLS
FPGA
FPGA Place&Route
Long compile times

## Slide 3: Introduction
Goal: enable FPGA usage by designers currently targeting GPUs and multi-cores
Problem: order-of-magnitude worse productivity
Productivity bottlenecks
  Register-transfer-level (RTL) design
    Solved by high-level synthesis (HLS)
  Long compile times (hours to days)
    Prevents mainstream methodologies
Solution: virtual architectures atop FPGAs (i.e. overlays)
  Provides near-instant place and route
    >1000x faster than FPGA vendor tools
  Integrates with HLS for rapid compilation
  Partial reconfiguration swaps in needed resources
  Enables transparent FPGA usage
> 1000x faster than FPGA vendor tools
OpenCL
HLS
Overlay
FPGA
__kernel void convolve(float *s) {…}
__kernel void kernelA(int *x) {…}
__kernel void kernelB(int *x) {…}
Overlay Place&Route

## Slide 4
CLIF High-Level Synthesis
Overlays could be integrated with any HLS tool
  Created our own tool: CLIF (OpenCL-IF)
  IF = intermediate fabric
CLIF compiles code onto reconfiguration contexts
  Definition: overlays that can be dynamically changed and swapped in&out of FPGA
  Contexts originally implemented using intermediate fabrics
  We now use supernet contexts

## Slide 5: CLIF Overview: Context Hit

## Slide 6: CLIF Overview: Context Miss

## Slide 7: CLIF Overview: Repeated Executions

## Slide 8: Results Summary
Evaluated system of 20 fixed and float kernels
  Up to 13,000x faster compiles
  0.15s per kernel
  2.5s vs 3.6 hours for whole system
  Enables runtime compilation
16.2% average clock overhead
60% less area than combined RTL implementations for each kernel
  Original IFs had significant area overhead
  New supernets use up to 8.9x smaller than minimum-sized IFs
  Rapid reconfiguration hides overhead of individual kernels

## Slide 9: Research Challenges
How to minimize area/performance overhead?
  CODES/ISSS 2010, ESL 2011, CASES 2012, ASAP 2013
How to create reconfiguration contexts for a given application or set of applications?
  IEEE Micro 2014, SHAW 14, FCCM 2015, TECS (to appear)
How to integrate with OpenCL high-level synthesis?
  IEEE Micro 2014, SHAW 14, FCCM 2015
How to customize overlay for different FPGA fabrics?
  CASES 2012, ASAP 2013, TECS (to appear)

## Slide 10: Catapult Collaboration
Just-in-time FPGA compilation
  Dynamic circuit optimizations based on changing workloads, inputs, etc.
  Portability of code across multiple FPGA types
Virtualization
  Rapid, transparent partial reconfiguration
  Improve productivity via virtual, application-specialized resources and interfaces
  Security
Application case studies

## Slide 11: References
  Coole, J. and Stitt, G. Adjustable-Cost Overlays for Runtime Compilation, FCCM 2015.
  Coole, J., and Stitt, G. Fast and flexible high-level synthesis from OpenCL using reconfiguration contexts. IEEE Micro: Special Issue on Reconfigurable Computing (Jan 2014).
  Coole, J., and Stitt, G. Opencl high-level synthesis for mainstream fpga acceleration. In Workshop on SoCs, Heterogeneous Architectures and Workloads (SHAW) 2014.
  Hao, L. and Stitt, G. Virtual Finite-State-Machine Architectures for Fast Compilation and Portability. ASAP’13, pp. 91-94.
  Landy, A., and Stitt, G. A low-overhead interconnect architecture for virtual reconfigurable fabrics. CASES ’12, pp. 111–120.
  Stitt, G., and Coole, J. Intermediate fabrics: Virtual architectures for near-instant FPGA compilation. Embedded Systems Letters, IEEE 3, 3 (sept. 2011), 81–84.
  Coole, J., and Stitt, G. Intermediate fabrics: Virtual architectures for circuit portability and fast placement and routing. CODES/ISSS ’10, pp. 13–22.

## Slide 12: Appendix

## Slide 13: Intermediate Fabric (IF) Overview
Synthesis
Bitfile
> 10k lookup-tables (LUTS)
FPGA specific: Not portable
FPGA
Lengthy compilation
Place & Route (PAR)
Traditional FPGA Tool Flow
Intermediate Fabric Tool Flow
Synthesis, Place & Route
Fast Compilation: several coarse-grained resources
. . .
Virtual Device
Physical Device
Physical Device(s)
Fast Partial Reconfiguration: even on devices without support
FPGA specific:
Limited portability
App Portability: always targets IF regardless of underlying FPGA

## Slide 14: CLIF Overview: Context Generation

## Slide 15
Use clustering heuristic based on k-means to sort by functional similarity
  We can ignore connections between functional units due to IF routing flexibilty
  Encourages op sharing within each group and merges ops used between kernels in group
  Merges ops of same type if “generics” can be configured (e.g. ALU) or promoted (e.g. width)
k # contexts provides a tuning parameter for tradeoffs based on designer intent
  Larger k  smaller, specialized contexts
  Can help fit: 60% decrease in context size going single  5 contexts in case study
  Can use savings to preemptively increase flexibility by growing each context
  144x faster reconfiguration vs. device (and KB vs. MB bitfiles)
Context Design Heuristic for IFs

## Slide 16
Ideally, contexts could also tailor their interconnect for the application at hand
  What if we included, at a minimum, interconnect to support communication requirements of source set…
  …using general-purpose routing as a fallback
   We can reduce network’s capacity (or eliminate it entirely) to minimize overhead 
    Goal: “only pay for what you want”
Supernet context family: includes merged ops and interconnect from source set and an optional secondary network
  Offline: merger combines source set datapaths so as to minimize added nets (and nodes), to create a supernet datapath
  Runtime: mapper attempts to match nets from incoming datapath to supernet, and handles anything else on the network
Supernets: Contexts w/ Tailored Interconnect