## Slide 1: OpenCL High-Level Synthesis for Mainstream FPGA Acceleration
James Coole
PhD student, University of Florida
Dr. Greg Stitt
Associate Professor of ECE, University of Florida
SHAW Workshop
This work is supported by National Science Foundation grant CNS-1149285 and the I/UCRC Program of the National Science Foundation under Grant No. EEC-0642422.

## Slide 2: Introduction
Numerous studies have shown performance, energy, and power advantages of FPGAs
  But, FPGA usage still limited to niche areas
  Goal: enable FPGA usage by designers currently targeting GPUs and multi-cores
Problem: 10x worse productivity
  Higher NRE costs than processor or GPU
  Increased time-to-market
  Niche usage, higher device costs
Productivity bottlenecks
  Register-transfer-level (RTL) design
    Requires specialized languages
    Requires cycle-by-cycle behavior
    Digital design expertise
  Low-level debugging
    Analyze cycle-by-cycle analysis of waveforms with 100s of signals
Specialized languages
Low-level debugging
Productivity Bottlenecks
Time consuming
Error prone

## Slide 3: Introduction
Potential Solution: high-level synthesis (HLS)
  Compile FPGA app from high-level code
  Significant recent achievements for OpenCL HLS
  But, still not appropriate for mainstream usage
Main problem: Long compile times
  Hours, days, even weeks
  Huge productivity bottleneck
  Prevents mainstream methodologies
  Prevents OpenCL’s runtime compilation
Need high-level synthesis that takes similar amount of time as software compilation
Mainstream High-level Code (e.g. OpenCL)
Problem:
Takes hours or days
Automatically creates RTL circuit

## Slide 4: Introduction
Solution: Intermediate Fabrics (IFs)
  Virtual, reconfigurable architectures between application and FPGA
    Hides low-level FPGA details
  Similar to coarse-grained reconfigurable arrays (CGRAs), but implemented on COTS FPGAs
    Cost and flexibility advantages
  Provides near-instant FPGA compilation via abstraction
    > 1000x faster than commercial tools
Integrates with OpenCL HLS to enable transparent FPGA usage
Main Contribution:
  Enables mainstream FPGA usage with near-identical tool flow
> 1000x faster than FPGA vendor tools

## Slide 5: Intermediate Fabric (IF) Overview
Synthesis
Bitfile
> 10k lookup-tables (LUTS)
FPGA specific: Not portable
FPGA
Lengthy compilation
Place & Route (PAR)
Traditional FPGA Tool Flow
Intermediate Fabric Tool Flow
Synthesis, Place & Route
Fast Compilation: several coarse-grained resources
. . .
Virtual Device
Physical Device
Physical Device(s)
Fast Partial Reconfiguration: even on devices without support
FPGA specific:
Limited portability
App Portability: always targets IF regardless of underlying FPGA
Main Research Challenge: Minimizing Overhead

## Slide 6
OpenCL-IF High-Level Synthesis
Intermediate fabrics could be integrated with any HLS tool
  We created our own tool: OpenCL-IF
OpenCL-IF compiles code onto reconfiguration contexts
  Definition: virtual architecture implemented atop FPGA
  Implemented using intermediate fabrics
    Other possibilities exist
Main research challenge: how to create intermediate fabrics/contexts for a given application or domain?
  Fast compilation assumes context already exists
  Without appropriate context, must use slow FPGA compilation

## Slide 7: OpenCL-IF Overview: Context Hit

## Slide 8: OpenCL-IF Overview: Context Miss

## Slide 9: OpenCL-IF Overview: Context Generation

## Slide 10: OpenCL-IF Overview: Repeated Misses

## Slide 11
Use clustering heuristic based on k-means to sort by functional similarity
  We can ignore connections between functional units due to IF routing flexibilty
  Encourages op sharing within each group and merges ops used between kernels in group
  Merges ops of same type if “generics” can be configured (e.g. ALU) or promoted (e.g. width)
k # contexts provides a tuning parameter for tradeoffs based on designer intent
  Larger k  smaller, specialized contexts
  Can help fit: 60% decrease in context size going single  5 contexts in case study
  Can use savings to preemptively increase flexibility by growing each context
  144x faster reconfiguration vs. device (and KB vs. MB bitfiles)
Context Design Heuristic for IFs

## Slide 12
OpenCL-IF Case Study
Xilinx ISE 14.4 using reduced effort for faster compilation at expense of circuit quality for XC6VCX130T-1FF1154. Times on quad-core 2.66 GHz Intel Xeon W3520 workstation with 12GB RAM running CentOS 6.4 x86 64.
Evaluated computer vision system with 10 fixed-/floating-point OpenCL kernels
  Compared OpenCL-IF compile times and area/performance against VHDL
On workstation, system compiles in ~3s total vs. 7.4h direct: 8700x speedup
  4x faster for FLT vs. FXD due to more device resources being hidden by IF cores
~0.15s per-kernel compile times show that runtime compilation is possible
1.8x system area overhead, 1.3x-15x per context vs. separate accelerators
  Overhead amortized over multiple kernels by using the IF’s rapid configurability
  Overhead decreases w/ new kernels!
  Lower for FLT vs FXD because of larger ops

## Slide 13
OpenCL-IF Case Study
Xilinx ISE 14.4 using reduced effort for faster compilation at expense of circuit quality for XC6VCX130T-1FF1154. Times on quad-core 2.66 GHz Intel Xeon W3520 workstation with 12GB RAM running CentOS 6.4 x86 64.
Same system evaluated using OpenCL-IF on an ARM embedded platform
  Single-core 1GHz Cortex A8
  Same Virtex 6 FPGA (using same contexts)
  Same program source and toolchain
System compiles in 20.7s total, still achieving 1470x speedup over workstation vendor synthesis
~1s per-kernel compile times show that runtime compilation is also possible on embedded devices
    Enables FPGA acceleration of OpenCL programs portable across devices and with dynamic workloads in embedded devices
    Embedded devices can’t generate new contexts themselves, but can request them from context servers

## Slide 14: Conclusions and Future Work
OpenCL-IF provides FPGA tool flow that is nearly identical to GPUs and multicores
  Enables near-instant (< 1s) FPGA compilation
  > 1000x faster than device-vendor tools
Performance overhead is modest
Area overhead can be significant for some use cases
  Significant focus of ongoing work
Future work
  Novel interconnect architectures to reduce area overhead
  High-level synthesis optimizations enabled by fast compilation
  Partial reconfiguration of fabric resources

## Slide 15: References
Coole, J., and Stitt, G. Fast and flexible high-level synthesis from OpenCL using reconfiguration contexts. IEEE Micro: Special Issue on Reconfigurable Computing (to appear).
Coole, J., and Stitt, G. Intermediate fabrics: Virtual architectures for circuit portability and fast placement and routing. CODES/ISSS ’10, pp. 13–22.
Landy, A., and Stitt, G. A low-overhead interconnect architecture for virtual reconfigurable fabrics. CASES ’12, pp. 111–120.
Stitt, G., and Coole, J. Intermediate fabrics: Virtual architectures for near-instant FPGA compilation. Embedded Systems Letters, IEEE 3, 3 (sept. 2011), 81–84.
Hao, L. and Stitt, G. Virtual Finite-State-Machine Architectures for Fast Compilation and Portability. ASAP’13, pp. 91-94.

## Slide 16
Improve developer productivity
  Typically involves multiple edits and in-board testing, requiring lengthy compilation for even minor changes
  Makes development more similar to GPUs and CPUs – difference is occasional creation of new contexts
    Large changes or accumulation of small changes results in temporary misses for affected kernels
    Reduces total compilation time across development
Increased portability and dynamic optimizations
  Runtime compilation allows application source to be portable between FPGAs and technologies
  Portable toolchain insulated from FPGA details
  Optimizations based on values known only at runtime
Context servers
  Because need for new contexts is likely to be bursty, makes sense to share context generation
  Lets systems incapable of FPGA PAR to handle misses
  Caching @ server might help decrease global miss rate
Envisioned Use Cases

## Slide 17
Memory Optimizations
Memory bandwidth often bottleneck in FPGA applications
  Specialized buffers can improve parallelism by > 10x
  e.g. sliding-window buffers [Fowers FPGA 2012]
Tool implements efficient buffer streaming by inferring 1/2D sliding-window buffers based on kernel’s use of memory
  Many kernels keep their memory accesses to some set of constant offsets relative to their workgroup id
  Easier to identify access patterns
  Schedules work items in sequence to ensure pattern
  Creates pipelined implementations in this case, with all control/memory interfacing external to IF
Similar analysis used to convert const-indexed __const memory to runtime-loaded constants

## Slide 18: Intermediate Fabric (IF) Architecture
Fabric can implement any architecture
  Current focus on island-style layout
    Switch boxes, connection boxes, tracks
  App-specialized computational units (CUs)
    FFTs, floating-point resources, filters, etc.
  Specialized track widths
Virtual Track
“Soft” RTL Track Implementation
For a n-bit track with m sources, circuit uses a m:1, n-bit mux
Many tracks in IF,
largest source of overhead
Island-Style Layout
tracks

## Slide 19: Intermediate Fabric (IF) Architecture, Cont.
Switch boxes implemented similarly
  Mux defines every connection
  Supports any topology
  Specialized to application requirements
Optional registers on outputs
  Eliminates combinational loops
  Minimizes delays across muxes
Pipelined interconnect can require complicated routing
  Ensures routing paths have same # of hops
For pipelined circuits, avoid by using realignment registers
  Lengthens shorter path, adds pipeline stages
  Enables use of traditional place & route algorithms
“Soft” RTL Switch Box

## Slide 20: Intermediate Fabric (IF) Tool Flow
Choose appropriate fabric:
1) Synthesize custom fabric
+ Low area overhead
- Requires one FPGA PAR
or
2) Select fabric from library
+ Fabric instantly available
- Possibly no appropriate IF
Implement IF on FPGA:
Soft resources implement virtual fabric as RTL code
+ Portable, flexible
- More overhead
2) Hard resources directly use physical routing resources
+ Less overhead
- Less portable, flexible
IF Creation Flow
App Design Flow
1 time only