## Slide 1: A Performance and Energy Comparison of FPGAs, GPUs, and Multicores for Sliding-Window Applications
Jeremy Fowers, Greg Brown, Patrick Cooke, Greg Stitt
University of Florida
Department of Electrical and Computer Engineering

## Slide 2: Introduction
Clear architectural trend of parallelism and heterogeneity
Heterogeneous devices have many tradeoffs
Usage cases also affect best device choice
Problem: huge design space
Problem
Solution
CPU
CPU
CPU
CPU
CPU
Problem
Solution
Execution time: 10 sec
Execution time: 2.5 sec
CPU
FPGA
PCI
CPU
GPU
PCI
Orders of Magnitude
Improvement
CPU
CPU
CPU
GPU
FPGA
Clock Rate
Base
Complexity
Base
Parallelism
Base
Power
Base
Execution Time
Task Size
Sequential CPU
Multicore CPU
GPU
FPGA
Huge Design Space
Which Accelerator?
Which Brand?
Number of cores?
Which Device?
Device Cost?
Design time?
Which algorithm?
Use case optimization?

## Slide 3: Case Study: Sliding Window
Contribution: thorough analysis of devices and use cases for sliding window applications
Sliding window used in many domains, including image processing and embedded
CPU
CPU
CPU
CPU
CPU
GPU
FPGA
Devices
Algorithms
Use Cases
Kernel Size
Image Size
Correntropy
Convolution
Sum of Absolute Differences

## Slide 4: Sliding Window Applications
We analyze 2D Sliding Window with 16-bit grayscale image inputs
Applies window function against a window from image and the kernel
“Slides” the window to get the next input
Repeats for every possible window
  45x45 kernel on 1080p 30-FPS video = 120 billion memory accesses/second
Window
Kernel
Window 0
Window Function
Output Pixel
Window W-1
Window 1
Input: image of size x×y, kernel of size n×m
for (row=0; row < x-n; row++) {
for (col=0; col < y-m; col++) {
// get n*m pixels (i.e., windows
// starting from current row and col)
window=image[row:row+n-1][col:col+m-1]
output[row][col]=f(window,kernel)
}
}

## Slide 5: App 1: Sum of Absolute Differences (SAD)
Used for: H.264 encoding, object identification
Window function: point-wise absolute difference, followed by summation
Kernel
W1
Window X
W2
W3
W4
k1
k2
k3
k4
W1
W2
W3
W4
k1
k2
k3
k4
d1
d2
d3
d4
a1
a2
a3
a4
Ox
Output Pixel
Absolute Value()
Ox = 0;
For pixel in window:
Ox += abs(pixeli – kerneli)

## Slide 6: App 2: 2D Convolution
Used for: filtering, edge detection
Window function: point-wise product followed by summation
Kernel
W1
Window X
W2
W3
W4
k1
k2
k3
k4
W1
W2
W3
W4
k4
k3
k2
k1
p1
p2
p3
p4
Ox
Output Pixel
Ox = 0;
For pixel in window:
Ox += (pixeli x kerneln-i)

## Slide 7: App 3: Correntropy
Used for: optical flow, obstacle avoidance
Window function: Gaussian of point-wise absolute difference, followed by summation
W1
W2
W3
W4
k1
k2
k3
k4
a1
a2
a3
a4
Ox
Output Pixel
Absolute Difference
Ox = 0;
For pixel in window:
Ox += Gauss(abs(pixeli – kerneli))
g1
g2
g3
g4
Gaussian Function()

## Slide 8: Devices Targeted
Type | Device | Board | Node | Host CPU | OS | Library
FPGA | Altera Stratix III E260 | GiDEL ProcStar III PCIe x8 | 65 nm | 2.26 GHz 4-core 45 nm Xeon E5520 | Red Hat Enterprise 5 64-bit Server | Quartus II 9.1
GPU | Nvidia GeForce GTX 295, Compute Capability 1.3 | EVGA PCIe x16 | 55 nm | 2.67 GHz 4-core Intel Xeon W3520 | Red Hat Enterprise 5 64-bit Server | CUDA Version 3.2
CPU | 2.67 GHz Intel Xeon 4-core W3520 | N/A | 45 nm | N/A | Windows 7 Enterprise 64-bit | OpenCL Intel SDK 1.1
Process nodes not the same; Devices are best of product cycle (2009)
FPGA host processor slower than CPU, GPU; host not used for computation
Windows 7 used for CPU instead of Linux; OpenCL Intel SDK 1.1 compatibility

## Slide 9: FPGA Architecture
Board
FPGA
Architecture accepts input image, kernel from CPU over PCIe
Streams from off-chip DDR RAM to on-chip Window Generator
Window Generator delivers windows to datapath
DDR2 RAM
Mem Control
Window Generator
Kernel Registers
Datapath
Mem Control
DDR2 RAM
Host CPU
PCIe Bus
Image Data
Kernel Data
Image Data
Kernel Data
Window Data

## Slide 10: Window Generator
I1,1
I1,2
I1,3
I1,4
I1,5
I2,1
I2,2
I2,3
I2,4
I2,5
I3,1
I3,2
I3,3
I3,4
I3,5
Window Generator
SRAM 1
SRAM 2
SRAM 3
I1,1
I1,2
I1,3
I2,1
I2,2
I2,3
I3,1
I3,2
I3,3
Register File
I1,5
I2,5
I3,5
I1,4
I2,4
I3,4
Must produce one window per cycle (up to 4 KB)
Allows datapath to compute one output/cycle
Capable of 400 GB/s throughput at 100 MHz
Sequential Image Data
For a 3x3 Kernel and 5x5 Image
Complete Windows

## Slide 11: Window Generator
When all windows involving row 1 are used, it is shifted out
The register file is then set to the first window of the next row
Continues until all windows are generated
Sequential Image Data
I1,1
I1,2
I1,3
I1,4
I1,5
I2,1
I2,2
I2,3
I2,4
I2,5
I3,1
I3,2
I3,3
I3,4
I3,5
For a 3x3 Kernel and 5x5 Image
Window Generator
SRAM 1
SRAM 2
SRAM 3
Register File
Complete Windows
I1,3
I1,4
I1,5
I2,3
I3,3
I2,4
I3,4
I2,5
I3,5
I4,1
I4,2
I4,3
I4,4
I4,5
I2,1
I2,2
I2,3
I3,1
I3,2
I3,3
I4,1
I4,2
I4,3

## Slide 12: FPGA Architecture
Board
FPGA
Architecture accepts input image, feature from CPU over PCIe
Streams from off-chip DDR RAM to on-chip Window Buffer
Window buffer delivers windows to datapath
Datapath computes one final output pixel per cycle
Results are stored to off-chip DDR RAM, retrieved by CPU over PCIe
DDR2 RAM
Mem Control
Window Generator
Kernel Registers
Datapath
Mem Control
DDR2 RAM
Host CPU
PCIe Bus
Image Data
Image Data
Image Data

## Slide 13: FPGA Datapaths
SAD datapath is fully pipelined up to 45x45 kernels:
  Point-wise subtract every window and kernel element
  Absolute value of the result
  Input to pipelined adder tree
2D Convolution replaces subtract and absolute operations with multiply, reverses order
  Fully pipelined up to 25x25 kernels

## Slide 14: FPGA Datapaths Cont.
Correntropy adds Gaussian, max value steps to pipeline
Gaussian approximated by 64-entry lookup table, provides necessary accuracy
Monitors output and stores 2 highest values

## Slide 15: GPU CUDA Framework
Based on previous work designed to handle similar data structure
  Achieved comparable speed for the same kernel sizes
  Allows larger kernel and image sizes
Created a framework for sliding window apps
Main challenge is memory access

## Slide 16: GPU CUDA Framework Cont.
Image stored in global memory (large capacity, slow reads)
Entire kernel stored, and an image subset, in each thread block’s shared memory (low capacity, quick reads)
Image subset is 32x16 Macro Blocks of 2x2 output pixels
Each thread handles one Macro Block (4 output pixels)
  Previous work used Macro Blocks of 8x8 output pixels

## Slide 17: GPU Implementations
SAD: each thread computes SAD between kernel and the 4 windows in its Macro Block
2D Convolution: like SAD, but with multiply-accumulate
2D FFT Convolution: used CUFFT to implement frequency domain version
Correntropy: adds Gaussian lookup table to SAD, computes max values in parallel post processing

## Slide 18: CPU OpenCL Implementations
Focused on memory management and limiting communication between threads
  Followed Intel OpenCL guidelines
Create a 2D NDRange of threads with dimensions equal to the output
Store image, kernel, output in global memory
Straightforward SAD, 2D Convolution, and Correntropy implementations
  Correntropy post-processes for max values
  FFT convolution found to be slower, not included

## Slide 19: Experimental Setup
Evaluated SAD, 2D Convolution, and Correntropy implementations for FPGA, GPU, and Multicore
Estimated performance for “single-chip” FPGAs and GPUs
Used sequential C++ implementations as a baseline
Tested image sizes with common video resolutions:
  640×480 (480p)
  1280×720 (720p)
  1920×1080 (1080p)
Tested kernels of size:
  SAD and correntropy: 4×4, 9×9, 16×16, 25×25, 36×36, 45×45
  2D convolution: 4×4, 9×9, 16×16, 25×25

## Slide 20: Application Case Studies Sum of Absolute Differences
FPGA performance consistent across kernels
GPU best at small kernels, FPGA best for large
Performance of all implementations scales with image size
Only FPGA gets real-time performance at high kernel sizes
30 FPS

## Slide 21: Application Case Studies 2D Convolution
Similar trends to SAD
FPGA and GPU-FFT performance consistent across kernels
GPU time domain best at small kernels, GPU-FFT best for large
Only FPGA gets real time performance at high kernel sizes
Notes: ----- Meeting Notes (2/20/12 09:46) -----
and gpu!

## Slide 22: Application Case Studies Correntropy
Very similar trends to SAD
Only FPGA gets real-time performance at high kernel sizes

## Slide 23: Speedup
Speedup for 720p over C++ baseline, 480p and 1080p data omitted
FPGA speedup increases with kernel size, up to 298x
FPGA up to 57x faster than OpenCL, 11x faster than GPU
GPU-FFT averages 3x faster than FPGA for 2D convolution
OpenCL speedup averages 4.2x over baseline CPU

## Slide 24: Single Chip Implementations
Results shown for 720p images
FPGA uses up to 64% of execution time on PCIe transfers
  Weakness of x8 PCIe bus
GPU uses up to 65%
  Communication amortized by lengthy computation of large kernels

## Slide 25: Energy Comparison
Sliding window often used in embedded systems
Energy calculated as (worst case power x execution time)
FPGA most efficient, lead increases with kernel size
GPU competitive despite much larger power consumption

## Slide 26: Future Work
Motivates our future work, which does this analysis automatically
Elastic Computing, an optimization framework, chooses the most efficient device for a given application and input size

## Slide 27: Conclusion
FPGA has up to 57x speedup over multicores and 11x over GPUs
Efficient algorithms such as FFT convolution make a huge difference
FPGA has best energy efficiency by far
FPGA architecture enables real-time processing of 45x45 kernels on 1080p video
Notes: Too much FPGA bias?