## Slide 1
Heterogeneous Parallel Programming
SYCL Accumulation Example
Greg Stitt
Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: SYCL Accumulation
+
+
+
+
+
+
+
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Basic idea:
  Each kernel adds two numbers
  Create tree of adders
  Write end result to a[0]
    a[]
    a[]

## Slide 3: SYCL Accumulation
+
+
+
+
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Problem:
  Can’t send data between kernel instances without storing in memory first
    Technically can use “pipes” on FPGAs, but not on other devices
  Must store outputs of each level of the adder tree back to memory
Where to store intermediate results?
  We first look at intuitive (but incorrect) technique
    a[] before:
    4 work-items
    Each adds 2 values
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] after:
    Iteration 0:

## Slide 4: SYCL Accumulation
+
+
+
+
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Repeat this strategy until number of sums “reduced “ to 1
    a[] before:
    2 work-items have no work to do
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] after:
    Iteration 1:

## Slide 5: SYCL Accumulation
+
+
+
+
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Repeat this strategy until number of sums “reduced “ to 1
Limitation: each iteration uses half the work-items of previous iteration
  Accumulation does not achieve full utilization of most devices.
    a[] before:
    3 work-items have no work to do
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] after:
    Result stored in a[0]
    Iteration 2:

## Slide 6: SYCL Accumulation
Why won’t this work?
  What happens if work-item 1 stores its result to a[1] before work-item 0 reads a[1]?
  Incorrect assumption that all work-items run at the same time, and are perfectly synchronized
  Also incorrect to assume work-items are scheduled in order of id
Important: work-items are not guaranteed to execute in any order
+
+
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
    1
    0
    a[1] is overwritten before work-item 0 does a[0] + a[1]
    a[0] now has incorrect data

## Slide 7: SYCL Accumulation
How do we fix this?
  Store intermediate sums so prevent overwriting data being read in other work-items
+
+
+
+
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] before:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] after:
    Iteration 0:
    0
    1
    2
    3

## Slide 8: SYCL Accumulation
How do we fix this?
  Store intermediate sums so prevent overwriting data being read in other work-items
+
+
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] before:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] after:
    Iteration 1:
    0
    1

## Slide 9: SYCL Accumulation
How do we fix this?
  Store intermediate sums so prevent overwriting data being read in other work-items
+
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] before:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] after:
    Iteration 2:
    0
    Result stored in a[0]

## Slide 10: SYCL Code
How do we fix this?
  Store intermediate sums so prevent overwriting data being read in other work-items
+
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] before:
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
    a[] after:
    Iteration 2:
    0
    Result stored in a[0]

## Slide 11: SYCL Accumulation Optimizations
Previous method is a good strategy for accumulation
Are there any ways to further improve performance?
What is the current bottleneck?
  Every work-item reads from and writes to global memory
    For each iteration for some work-items
Optimization: can we leverage local memory?
  Lower latency than global
  Less contention from fewer work-item accesses
Strategy:
  Partition input array into sections
  Have work-group/compute-unit process each section using previous strategy
Remaining challenge:
  Where to store outputs of each work-group?